## Slide 1: PhD Course: Copernicus Uptake Use of satellite images for mapping and monitoring the hydrogeological changes in the framework of the A.M.AL.PI.18 Interreg Cooperation Programme
Federica Marotta – 35° cycle
Architecture, Built Environment and Construction Engineering (ABC) dept.
Supervisor: Cristiana Achille Tutor: Marco Scaioni
06 april 2022

## Slide 2
FRAMEWORK

## Slide 3
FRAMEWORK
IFFI project reference period: 1116 – 2017

## Slide 4
FRAMEWORK
Gotthardpass
Malojapass

## Slide 5
GOAL
What: Hydrogeological changes detection
How: Using Sentinel-2 images and a supervised classification technique
General idea: Conducting regular period analyses to reconstruct the evolution of hydrogeological changes in the area of interest
Simplified idea: Use of two images to identify changes in the landscape

## Slide 6
METHODOLOGY
Choice of images
QGis
Band Stacking
QGis
Image enhancement
QGis
RStudio
QGis
QGis
Training samples creation
Random Forest Classification
Post-processing of the classified image – Majority filter
Post processing of the classified image - Sieve
Open hub Sentinel 2

## Slide 7
CHOICE OF IMAGES
Satellite platform:
Sentinel 2-A and 2-B
Ingestion period:
06/2015 – 12/2021
Max cloud coverage:
30%
Area:
2463
MGRS location:
32TMS
32TNS
Selected images:
16/06/2018 TNS
15/06/2021 TNS

## Slide 8
CHOICE OF IMAGES
StorMe – Catasto degli eventi naturali Cantone Ticino
IFFI – Inventario dei Fenomeni Franosi in Italia

## Slide 9
CHOICE OF IMAGES

## Slide 10
BAND STACKING
16/06/2018 TNS
15/06/2021 TNS
+
v. 3.16.16
1
2
3
4
5
6
7
8
11
12
13
14
15
16
17
18
9
10
19
20

## Slide 11
IMAGE ENHANCEMENT
v. 3.16.16
Multi-temporal false color composite:
Red band: Band 19 (SWIR1 – date 2*)
Green band: Band 9 (SWIR1 – date 1)
Blue band: Band 11 (Blue – date 2)
* Date 1= 16/06/2018
Date 2= 15/06/2021
Date 1
Date 2
Creation of Savogno road
New cultivated field

## Slide 12
IMAGE ENHANCEMENT
v. 3.16.16
Date 1
Date 2
Villa di Chiavenna landslide (2019)
Multi-temporal false color composite:
Red band: Band 19 (SWIR1 – date 2)
Green band: Band 9 (SWIR1 – date 1)
Blue band: Band 11 (Blue – date 2)

## Slide 13
IMAGE ENHANCEMENT
v. 3.16.16
Date 1
Date 2
Val Madra landslide
Multi-temporal false color composite:
Red band: Band 19 (SWIR1 – date 2)
Green band: Band 9 (SWIR1 – date 1)
Blue band: Band 11 (Blue – date 2)

## Slide 14
v. 3.16.16
Date 1
Date 2
Gallivaggio rockfall (2018)
Lesina stream flood (2019)
IMAGE ENHANCEMENT
Multi-temporal false color composite:
Red band: Band 19 (SWIR1 – date 2)
Green band: Band 9 (SWIR1 – date 1)
Blue band: Band 11 (Blue – date 2)

## Slide 15
v. 3.16.16
Class | N. Samples
11 | 8
12 | 13
21 | 9
22 | 5
23 | 9
33 | 6
42 | 2
44 | 2
TRAINING SAMPLES CREATION

## Slide 16
v. 4.1.2
Random Forest:
a large number of individual decision trees that operates as an ensemble
Decision tree:
«What feature will allow me to split the observations at hand in a way that the resulting groups are as different from each other as possible (and the members of each resulting subgroup are as similar to each other as possible)?»
RANDOM FOREST CLASSIFICATION ALGORITHM

## Slide 17
v. 4.1.2
The script was written by Ned Horning [horning@amnh.org]
Support for writing and maintaining this script comes from The John D. and
Catherine T. MacArthur Foundation and Google.org.
The script was modified by Amber McCullum: NASA ARSET
Approximate number of training samples to be randomly selected for running the Random Forest algorithm:
100 for each class
Processing time: 6.83 min
RANDOM FOREST CLASSIFICATION ALGORITHM

## Slide 18
RANDOM FOREST CLASSIFICATION ALGORITHM
v. 4.1.2

## Slide 19
POST PROCESSING – MAJORITY FILTER
v. 3.16.16
Aim of the filter: to remove speckles and noise
Operation method:

## Slide 20
POST PROCESSING – MAJORITY FILTER
v. 3.16.16
Stacked
No filter
Majority filter 3x3
Majority filter 5x5

## Slide 21
v. 3.16.16
Majority filter 3x3
Majority filter 5x5
POST PROCESSING – MAJORITY FILTER
Stacked
No filter

## Slide 22
POST PROCESSING – SIEVE
v. 3.16.16
Aim of the algorithm: to remove small clumps of pixels incorrectly classified:
e.g., removal of group of pixels smaller than 3
3
..Replace them with the pixel value of the largest neighbour polygon
Set the 8-connectedness and threshold = 10 (default)

## Slide 23
v. 3.16.16
No filter
Majority filter 5x5
Majority filter 3x3
+
Sieve
POST PROCESSING – SIEVE
Majority filter 3x3

## Slide 24
v. 3.16.16
No filter
Majority filter 5x5
Majority filter 3x3
+
Sieve
POST PROCESSING – SIEVE
Majority filter 3x3

## Slide 25
DISCUSSION – QUALITATIVE ANALYSIS
The same vegetated area, in different light conditions, gives rise to a «non forest to non forest» incorrect classification
The presence of clouds generates confusion in the classification
2018
2021
2018
2021

## Slide 26
DISCUSSION – QUALITATIVE ANALYSIS
«Forest to non forest» changes (red) are quite well detected but little bit overestimated
2018
2021
2018
2021

## Slide 27
DISCUSSION – QUALITATIVE ANALYSIS
«Non forest to forest» (yellow) and «non forest to non forest» (green) show general error in the classification
2018
2021
For - For
For - Non For
Non For - Non For
Non For - For

## Slide 28
Clouds removal to perform a more precise classification
Choice of images with < cloud coverage to perform a better classification
Change the approximate number of training samples to be randomly selected for running the Random Forest algorithm
Try to add/remove classes to the classification
Try to classify a 21 stacked bands raster (: NDVI2021-NDVI2018)
Try the three different supervised classification in Qgis environment (SCP plugin)
Perform a validation of the classification
FUTURE WORKS

## Slide 29
Mobile GIS in support of Copernicus EMS
Use of Qfield and Input app to map in real time changes occured in the environment
FAR FUTURE WORKS

## Slide 30
Thank you!